## Slide 1: Accelerating Finite Difference Computations Using General Purpose GPU Computing Date: 7 November 2012
POC: James D. Stevens
559th SMXS/MXDECC
Phone: 405-736-4051
Email: james.stevens@tinker.af.mil
I n t e g r i t y - S e r v i c e - E x c e l l e n c e
TEAM TINKER
OKLAHOMA CITY
AIR LOGISTICS COMPLEX

## Slide 2: Background
Presenter: Jim Stevens
  MS in Computer Science, 2011, School of Engineering and Applied Science at Washington University in St. Louis
  76th Software Maintenance Group at Tinker AFB
Mission: maintain software on weapon systems
  Support the warfighter!
Supercomputing resources 660core/3.5 TFLOPS
  Recycled computer systems ($75 initial budget)
GPGPU programming with CUDA

## Slide 3: Outline
Goal: accelerate weather prediction model
  History of optimization efforts
A look at the GPU
  Can it help reduce real time computing requirements?
GPU programming approach
  Basic overview
Our case study and results
  Techniques for optimization
  Results/evaluation
    Weather calculations
    EM wave calculations
Road map for future work

## Slide 4: Weather Model
U,V,W represent winds
Theta represents
temperature
represents pressure
T – Time
X – east west direction
Y – north south direction
Z – vertical direction
Turb – turbulence terms (what can’t be measured/predicted)
S – Source terms, condensation, evaporation, heating, cooling
D – numerical smoothing
f – Coriolis force (earth’s rotation)
Navier Stokes Equations
Others variables include soil, cloud and precipitation processes

## Slide 5: Past Optimization Attempts
Vector processors: 50-90% peak – fast memory
  Loop Merging – removing operators from the code
  Loop Fusion – helps the compiler vectorize code
Scalar: 10-60% peak – memory bound
  Loop Merging – reduces number of loads and stores
  Supernoding/Tiling
    Data/cache reuse
      Rearrange computations for maximum data reuse
References:
  OSCER Symposium (Weber: 2005,2006,2008)
  Linux Cluster Institute (Weber and Neeman: 2006)

## Slide 6: Past CPU Results
Notes: -scalar processors
-2009 (graph)

## Slide 7: The GPU
(graphics processing unit)

## Slide 8: NVIDIA Tesla C1060 GPU
Tesla C1060 GPU has 240 cores
30 Multiprocessors (MP)
  8 cores each
Registers on each MP
  Accessible to all 8 cores
Goal: Utilize all GPU cores
  >80% core utilization on loops

## Slide 9: CPU - GPU Comparison
Single core CPUs capable of ~10 GFLOP/s
Multicore capable of ~100’s GFLOP/s
But CPU memory bandwidth severely restricts real world performance of multicore CPUs for memory intensive applications
GPUs offer > 1 TFLOP/s potential
The coding style for GPGPUs is very different
“New language” (CUDA / OpenCL) needed for programming on GPU
CUDA = Compute Unified Device Architecture

## Slide 10: Learning CUDA
“Manual” GPGPU programming is hard (at first)
  “Automatic” GPGPU programming – add directives surrounding loops
    Compiler attempts to parallelize the loop
    Rarely yields best results
  “Manual” GPGPU programming – write GPU code yourself
    More difficult
    Faster code, more customizable
    Disclaimer: this is not a CUDA class
      Goal: understand basic CUDA/GPGPU programming concepts well enough to decide whether or not it has the potential accelerate your code
Notes: Compute Unified Device Architecture (CUDA) is a parallel computing architecture developed by Nvidia for graphics processing.

## Slide 11: CUDA Threads
Thread = a single instance of computation
  One thread per processor-core at a time
CUDA allows you to specify the thread organization, count, and indexing
  You control which threads are responsible for which portion of the task

## Slide 12: GPU Memory Components
Global Memory
  Main memory, 4 GB for the NVIDIA Tesla C1060
  About 200 cycles to access (vs. 50 cycles for a CPU)
Registers
  64KB per multiprocessor (vs. 512 B for Pentium 4 CPU)
  1 cycle to access
Shared registers (AKA “shared memory”)
  16 KB per multiprocessor
  Can be allocated for each block of threads
  All threads within block can access all data in shared registers, even if another thread fetched it
  Allows for data reuse – this is important
Notes: -There are other types of memory but we’re not discussing them

## Slide 13: General CUDA Program Format
Step 1 – copy data from CPU main memory to GPU global memory (from host to device)
Step 2 – threads run code inside kernel function
  Each thread fetches some data from global memory and stores it in registers
  Each thread performs computations
  Each thread stores a result in global memory
Step 3 – copy results from device back to host

## Slide 14: Simple CUDA example
We want to increment each element in a 1-dimensional array of integers
CPU Approach
Create/initialize array
Perform loop
do i = 1,n
array(i) = array(i)+1
end do
GPU Approach
Create/initialize array
Copy array data to GPU memory
Create n threads
Have each thread do the following:
array[threadIDX] =
array[threadIDX] + 1
Copy array back to host
threadIDX is the thread’s unique thread index
Threads may execute in any order
Notes:   The code that each individual thread executes goes inside a function called the kernel
  All threads will execute the same kernel
    Threads may execute in ANY order
  How do you split up the work?
    Within the kernel, you can access thread indexing variables - thread index, block dimensions, block index, grid dimensions
    Use these variables to control which subset of the data that particular thread accesses
      See threadIDX variable in example

## Slide 15: Simple CUDA Example
Any questions at this point?

## Slide 16: Weather Model Equations
U,V,W represent winds
Theta represents
temperature
represents pressure
T – Time
X – east west direction
Y – north south direction
Z – vertical direction
Turb – turbulence terms (what can’t be measured/predicted)
S – Source terms, condensation, evaporation, heating, cooling
D – numerical smoothing
f – Coriolis force (earth’s rotation)

## Slide 17: Solving Weather Model Equations
DO k = 3,nz-2
DO j = 3,ny-2
DO i = 3,nx-2
u(i,j,k,2)= -u(i,j,k,2)*... ( 150 operations )
! compute uadv u (... 18 operations ...)
! compute vadv u (... 16 operations ...)
! compute wadv u (... 16 operations ...)
! compute cmixx u (... 33 operations ...)
! compute cmixy u (... 33 operations ...)
! compute cmixz u (... 33 operations ...)
v(i,j,k,2)= -v(i,j,k,2)*... ( 148 operations )
w(i,j,k,2)= -w(i,j,k,2)*... ( 100 operations )
p(i,j,k,2)= -p(i,j,k,2)*... ( 49 operations )
pt(i,j,k,2)= -pt(i,j,k,2)*... ( 148 operations )
595 operations total
CPU Version
Normally, these computations are done separately, why combine them?
  Data reuse!
Notes: Triple loop, all elements in 5 arrays get updated. As an example, we’ll look at the first part of the u update more closely…
(note: In the original calculation, these are not all done in the same loop. We’re testing to see how fast we can do them all at once.)
*WHY put these computations together? Data reuse!

## Slide 18: Stencil Data Requirements
u(i,j,k,2)= -u(i,j,k,2)*rk_constant1(n)
! compute uadv u
+tema4*( (u(i,j,k,1)+u(i+2,j,k,1))
*(u(i+2,j,k,1)-u(i,j,k,1))
+(u(i,j,k,1)+u(i-2,j,k,1))
*(u(i,j,k,1)-u(i-2,j,k,1)) )
-temb4*( (u(i+1,j,k,1)+u(i,j,k,1))
*(u(i+1,j,k,1)-u(i,j,k,1))
+(u(i,j,k,1)+u(i-1,j,k,1))
*(u(i,j,k,1)-u(i-1,j,k,1)) )
Subset of calculation – u array – uadv u
Note: For every (i,j,k) element, this part of the update requires the value at (i,j,k), as well as 4 other values – the two on either side of (i,j,k) in the i direction: (i-2,j,k) (i-1,j,k) (i+1,j,k) (i+2,j,k)

## Slide 19: U Calculation – elements needed
 | Arrays | Direction of adjacent values
uadv u | u | i
vadv u | u, v | j
wadv u | u, w | k
cmixx u | u, ubar | i
cmixy u | u, ubar | j
cmixz u | u, ubar | k
i
j
k
ALL elements needed to update u(i,j,k)
u
Notes: All the adjacent values required to update one element.

## Slide 20: Global Memory Access (i-calculations only)
Normal registers - each thread will fetch five elements from global memory
  That’s inefficient - each element would be fetched 5 times by 5 different threads
Shared registers - Each thread copies one element into a “shared” array (stored in shared registers) that can be accessed by all threads
  Shared arrays allocated/accessed within block
Then each thread only performs one global fetch and can access all 5 elements it needs!

## Slide 21: Shared Memory Limitation
Limited to 16 KB of shared registers
  We’re processing gigabytes of data
  Need to break up the problem into smaller pieces that can be moved in and out of shared memory efficiently
What else do we need to do to get maximum performance?

## Slide 22: Strategies for Performance
Make sure global memory fetches are coalescing
  When adjacent threads access adjacent locations in global memory, the fetches are “coalesced” automatically into a single large fetch
  Absolutely necessary for good performance
  Number 1 priority

## Slide 23: Strategies for Performance
Reuse as much data as possible
  By using shared registers
    Break problem into pieces that are small enough to fit into shared memory
  By having threads perform cleverly designed loops
    Not using shared registers
    Loops within threads that solve the following problem…

## Slide 24: Data Reuse Through Looping
To maximize coalescence, we need blocks of threads that are “long” in the i-direction.
However, because of our size limitation on shared memory, this forces blocks to be “narrow” in the other two dimensions.
  64x1x1, for example
This is a problem for the parts of the calculation that require neighboring data in the j and k directions
  Can we still reuse data for these parts of the calculation?
  Yes! Partially. We can combine the i and j calculations

## Slide 25: Data Reuse: Looping + Shared Registers
Use shared registers to reuse data needed for “i-calculations”
Have each thread loop in the j-direction to reuse data needed for the “j-calculations”
in registers
































































i
k
j
threads
Each element is only fetched once from global memory, and then used nine times (see animation)
shared registers
Best viewed with animations
Notes: Make sure to view this with the animations.

## Slide 26: Other Strategies for Performance
“Hide” memory fetches with computations
  Structure kernel so that data is being fetched while computations are being performed (the scheduler will try to help with this)
Choose block dimensions that allow for maximum thread-scheduling efficiency
  Multiples of 32 threads
  Blocks that are “longer” in one dimension (i) to facilitates maximum coalescence

## Slide 27: Strategies for Performance
Designing your program so that it uses all of these strategies is difficult
  It’s a bit like trying to design a car that is luxurious, safe, fast, agile, reliable, practical, inexpensive, visually appealing, and fuel efficient all at the same time
    There are tradeoffs - you have to find the right balance
    Experiment

## Slide 28: Weather Computation - Results
Chart: Speed (GFLOP/s)
| CPU (All 595 Operations) | GPU (All 595 Operations) | GPU (399 Operation Subset)
Excluding Host-Device Mem. Transfer | 3.1 | 181 | 255
Including Host-Device Mem. Transfer | 8.3 | 6.5

## Slide 29: Host-Device Data Transfer
Huge bottleneck
What can we do?
  Hide data transfer behind CPU computations
    Transfer data while CPU is performing other necessary work
  Hide data transfer behind GPU computations
    Transfer a piece of the data to the GPU
    Begin performing GPU computations while the next piece of data is being transferred
Currently working on this

## Slide 30: Evaluating Results
How do we evaluate our results?
Estimate theoretical hardware peak
  933 GFLOP/s for single precision
  But we can’t use some of the hardware
    No texturing, reduces peak by about 33%
  This number assumes we’re taking advantage of the fused multiply-add instruction, but our computation doesn’t have many multiply-adds
    Reduces peak by about 50%
  So achievable hardware peak is about 311 GFLOP/s
  Kernel runs at 82% of peak, not bad!!!

## Slide 31: Estimating Application Speed Limit
Determine theoretical application “speed limit”
Based on global memory bandwidth and algorithm memory requirements
  Even if our algorithm has 100% data reuse and we completely hide all operations behind data fetches, we would still need to fetch each element of data from global memory one time, and write our results back
  Compute time required to move data
    T = (data moved) / (global memory bandwidth)
  Compute speed limit (FLOP/s)
    ASL = (Algorithm FLOP Count) / T

## Slide 32: Application Speed Limit
  786 GFLOP/s for the 399 operation subset (Tesla C1060 GPU)
  Because this computation has such a high operation-to-memory-fetch ratio (OMFR), ~30:1, this “speed limit” is high
  This is higher than our achievable hardware peak, which means our performance might increase if the GPU had faster multiprocessors
  Suggests that our program is not memory bound
This peak can be calculated before writing any code to find out if a particular computation is a good candidate for GPU acceleration
  Increment array example: 12.8 GFLOP/s = poor candidate

## Slide 33: Maxwell’s Equations
DO k = 3, nz-2
DO j = 3, ny-2
DO i = 3, nx-2
hx(i,j,k) = da * hx(i,j,k) + db * ( (ez(i,j,k) - ez(i,j+1,k) ) * deny
+ (ey(i,j,k+1) - ey(i,j,k) ) * denz )
hy(i,j,k) = da * hy(i,j,k) + db * ( (ez(i+1,j,k) - ez(i,j,k) ) * denx
+ (ex(i,j,k) - ex(i,j,k+1) ) * denz )
hz(i,j,k) = da * hz(i,j,k) + db * ( (ey(i,j,k) - ey(i+1,j,k) ) * denx
+ (ex(i,j+1,k) - ex(i,j,k) ) * deny )
…
!! Three loops for ex, ey, ez

## Slide 34: Maxwell’s Equations - Results
Chart: Speed (GFLOP/s)
| CPU (All 595 Operations) | GPU (All 595 Operations)
Excluding Host-Device Mem. Transfer | 1.5 | 32.1
Including Host-Device Mem. Transfer | 2.1

## Slide 35: Evaluating Results
  Observed top speed – 32.1 GFLOP/s
  Achievable hardware peak – 311 GFLOP/s (unchanged)
  OMFR (operation-to-memory-fetch-ratio) – 2.67:1
    vs. 30:1 for the weather calculations
  ASL (application speed limit) – 68.6 GFLOP/s
  The ASL is less than the achievable hardware peak
  Achieved 47% of the ASL
  The OMFR (and thus, the ASL) for this calculation is 11.2 times smaller than the OMFR for the weather calculations, and it runs 8 times slower
  This computation may be a reasonable candidate for GPU acceleration, but the speedup will be much greater for the weather calculations (due to their higher OMFR)

## Slide 36: Good Candidates for GPU Acceleration
Easily parallelizable
  Same set of independent operations are performed on each element in a domain (SIMD)
  These operations can execute in any order
Spatial locality
  Individual operations require data that is nearby in the domain
  Facilitates data reuse
High operation-to-memory-fetch ratio
  Calculate theoretical “speed limit” based on algorithm memory requirements and global memory bandwidth

## Slide 37: Potential Future Work
Deal with the host-device memory transfer bottleneck
Add other big time-step computations for weather computation
  Turbulence, coriolis, buoyancy
  Cloud physics
  Radiation
Include small time-step
  Texture/interpolators for the pressure gradient
Parallel version (MPI)

## Slide 38: Resources for Learning CUDA
  Programming Massively Parallel Processors: A Hands-On Approach by Kirk and Hwu
  On Books 24x7
  Online lecture slides and audio
  ECE 498 AL (Univ. of Illinois)
  NVIDIA CUDA Programming Guide
  Portland Group CUDA Fortran Programming Guide and Reference
Forums
  Portland group
  NVIDIA

## Slide 39
TEAM TINKER